หัวข้อวิทยานิพนธ์	ระบบผลิตกระแสไฟฟ้าพลังงานแสงอาทิตย์สำหรับโน้ตบุ๊ก

หน่วยกิต	12

ผู้เขียน			นายพุฒิสรรค์   อนุกูลพันธ์

อาจารย์ที่ปรึกษา		รศ.ดร.ธเนศ   ธนิตย์ธีรพันธ์

ผศ.ดร.คมกฤตย์   ชมสุวรรณ

หลักสูตร	ครุศาสตร์อุตสาหกรรมมหาบัณฑิต

สาขาวิชา	วิศวกรรมไฟฟ้า

ภาควิชา	ครุศาสตร์ไฟฟ้า

คณะ	ครุศาสตร์อุตสาหกรรมและเทคโนโลยี

พ.ศ.	2552

บทคัดย่อ

งานวิจัยนี้ เป็นการนำเซลล์แสงอาทิตย์มาผลิตเป็นแหล่งจ่ายกระแสไฟฟ้าให้กับคอมพิวเตอร์โน้ตบุ๊ก โดยใช้ไมโครคอนโทรเลอร์ในการควบคุมการทำงาน ซึ่งแหล่งจ่ายกระแสไฟฟ้านี้ได้ออกแบบมาสำหรับรับแรงดันไฟฟ้ากระแสตรงทางด้านอินพุตที่ 18 โวลต์ ที่มาจากการประยุกต์ใช้งานเซลล์แสงอาทิตย์ในประเทศไทย ทำให้ราคาลดลงและสามารถใช้งานได้ตลอดทั้งปี และมีขนาดของเซลล์แสงอาทิตย์ที่มีขนาดเล็กลงและถูกออกแบบให้สามารถเคลื่อนที่และนำไปใช้กับคอมพิวเตอร์โน้ตบุ๊กได้อย่างสะดวกในการใช้งานในด้านต่างๆ และสามารถผลิตกระแสไฟฟ้าให้กับคอมพิวเตอร์โน้ตบุ๊กให้สามารถใช้งานได้อย่างต่อเนื่อง เนื่องมาจากปกติคอมพิวเตอร์โน้ตบุ๊กจะมีระยะการใช้งานได้สั้นอันเนื่องมาจากปริมาณการใช้กระแสไฟฟ้าที่สูง ซึ่งงานวิจัยนี้ได้ใช้เซลล์แสงอาทิตย์ ขนาด 18 โวลต์ 0.5 แอมแปร์ วงจรดีซีทูดีซี คอนเวอร์เตอร์ สามารถผลิตแรงดันได้ 20 โวลต์ 60 วัตต์ และใช้คอมพิวเตอร์โน้ตบุ๊กขนาด 20 โวลต์ 3.25 แอมแปร์ ใช้วงจรดีซีทูดีซี บูส คอนเวอร์เตอร์ในการศึกษา โดยใช้เทคนิคการสวิตซ์ โดยอุปกรณ์ MOSFET และการใช้ไมโครคอนโทรเลอร์ ตระกูล PIC ในการควบคุมการทำงานและผลิตแรงดันทางด้านเอาต์พุต 20 โวลต์

ซึ่งจากการทดลอง วงจรในงานวิจัยนี้ใช้วงจรดีซีทูดีซี บูส คอนเวอร์เตอร์จากรายละเอียดที่ระบุไว้ข้างต้น ที่ระดับแรงดันทางด้านอินพุท 17 โวลต์และ 20 โวลต์ทางด้านเอาต์พุทและผลิตกำลังไฟฟ้าทางด้านเอาต์พุต 60 วัตต์ และสามารถควบคุมแรงดันที่มีการเปลี่ยนแปลงจากทางด้านอินพุต ให้มีแรงดันคงที่ที่ 20 โวลต์ โดยใช้เทคนิคการควบคุมค่าดิวตี้ไซเคิ้ล ที่ความถี่ 19 กิโลเฮิร์ต

คำสำคัญ: เซลล์แสงอาทิตย์/คอมพิวเตอร์โน้ตบุ๊ก/บูส ดีซี ทู ดีซี คอนคอนเวอร์เตอร์

Thesis Title	Photovoltaic Power Supply for Laptop Computer Based on Microcontroller Controlled Boost Converters

Thesis Credits	12

Candidate	Mr. Puttisun  Anukhoolphant

Thesis Advisor	Asoc. Prof. Dr. Tanes  Tanitteerapan

Asst. Prof. Dr. Komkrit  Chomsuwan

Program	Master of Science in Industrial Education

Field of Study	Electrical Engineering

Department	Electrical Technology Education

Faculty	Industrial Education and Technology

B.E.	2552

Abstract

This Paper, the photovoltaic power supply for laptop computer base on microcontroller

Controlled boots converters was proposed. The proposed power supply was designed for DC input voltage at 18 volts that is available for photovoltaic applications. In Thailand, solar energy is not taken more cost and can get in everyday in all year. Then, applications of photovoltaic are interesting to develop for many site areas. Laptop computer area also should be considered to be supported by photovoltaic applications due to it is very convenient if we can bring the computer to work in everywhere even there is a remote area where on the power utility. Usually, the computer almost consume power energy from the power utility that has some inconvenient in remote distance installation, and having more power energy consuming. The power supply was consisted of a solar array rated 18V and 0.5A. A DC-DC boost converter regulating output voltage as 20V at 60W, and a laptop computer having rated at 20V and 3.25A. The DC-DC boost converter was selected to study and implementation in this paper. The boost switch, which is typically a MOSFET, was controlled by PIC series microcontroller to regulate the output voltage at 20V.

To verify the proposed power supply, a circuit implementation of 60 Watts of the charger based on Dc-DC boost converter as specifications following 17 VDC of input voltage, 20 VDC of output voltage, 60 watts of power output, was applied. The circuit control was operated as keeping 20VDC by varying the duty ratio at 19KHz of switching frequency by microcontroller.

# Text boxes

Keyword: Photovoltaic power supply, PC notebook power supply, DC-DC converter